## Slide 1: Solar PV Installation and Maintenance
Notes: VO: Welcome to this course on Solar PV Installation and Maintenance.

## Slide 2
Course Navigation
Notes: VO: Here you will understand the navigation of the course. Hover on each option on the screen to know more.

## Slide 3
Notes: VO: Hello, I am Maya and I will be your guide for this course

## Slide 4
Course Description
Duration (Hrs)
Audience
This course helps you to learn how to install, connect, test, and maintain a solar PV system.
Click each tab to know more.
Course Introduction
Notes: Duration: 2 hrs Audience: This course is for Technicians and whoever would like to learn how to install the solar PV system. VO: Welcome to Solar PV Installation and Maintenance course. In this course, you will learn how a solar system is installed and made ready for use. You will see each step, understand why it is done, and learn how to perform it correctly on-site.

## Slide 5
Identify the main steps and components of solar PV installation
Apply correct methods for wiring, setup, and testing
Understand how systems are installed and connected
Follow safe practices and perform basic system checks
By the end of this course, you will be able to:
Course Objective

## Slide 6: Key Terms
Stores electricity so it can be used at night or on cloudy days.
Electricity used in homes and offices. Fans, lights, and TVs.
Electricity that flows in one direction. Solar panels make DC.
Electricity that flows in one direction. Solar panels make DC.
Changes solar DC into electricity that home
machine.
A system that uses sunlight to make electricity.
Electricity used in homes and offices. Fans, lights, and TVs.
Electricity that flows in one direction. Solar panels make DC.
Electricity that flows in one direction. Solar panels make DC.
Mounting Structure
Array
Alignment
Cable Routing
DC Cabling
System Integration
AC Wiring
Distribution Board (DB)
Connection Tightening
Continuity Test
Insulation Test
System Start-up
Notes: VO: Here are the key terms used in the course. Click each term to know more about each of them.

## Slide 7: Key Terms
Stores electricity so it can be used at night or on cloudy days.
Electricity used in homes and offices. Fans, lights, and TVs.
Electricity that flows in one direction. Solar panels make DC.
Electricity that flows in one direction. Solar panels make DC.
Changes solar DC into electricity that home
machine.
A system that uses sunlight to make electricity.
Commissioning
PPE
Routine Maintenance
Preventive Maintenance
Inspection
Reporting
Remote Monitoring
System Performance
Notes: VO: Here are the key terms used in the course. Click each term to know more about each of them.

## Slide 8: Installation Process Overview
Sunlight falls on solar panels
Structure
Panel
Wiring
Inverter
Testing
Panels generate DC electricity
Inverter converts DC to AC
AC power runs appliances
Video
Notes: VO: Before we begin, let’s first understand the overall installation process. A solar system is installed step by step, starting from the structure, then panels, followed by wiring, inverter setup, and finally testing. We will go through each of these steps one by one in this course.

## Slide 9: Pre-Installation: Site Survey & Vendor Planning
Check rooftop space, strength, and sunlight exposure
Finalize vendor and system design
Video to be embedded PM Surya Ghar Full Video 0:00 seconds to 00:46 (crop this part)
Notes: VO: First, we assess the rooftop to check space, strength, and sunlight exposure. Then, based on this, we finalize the vendor and system design for the site.

## Slide 10: Mounting Structure Installation
Base of the solar system
Supports and holds panels in place
Video to be embedded PM Surya Ghar Full Video
0:46 seconds to 10:00
Notes: VO: Let’s start with the mounting structure, which acts like the foundation of the system. Just like a weak foundation can affect a building, if the structure is not fixed properly, the panels may become loose or misaligned. Now watch how the mounting structure is installed step by step. Notice how proper alignment and fixing ensure a strong and stable base.

## Slide 11: Check your Understanding
A technician installs the mounting structure without checking alignment properly. What is the most likely long-term issue?
A. Faster power generation
B. Panels may become loose or misaligned
C. Increased battery backup
D. Improved inverter efficiency
Correct Answer: B

## Slide 12: Check your Understanding
Why is the mounting structure compared to the foundation of a building?
A. It stores electricity
B. It powers the inverter
C. It supports and stabilizes the entire system
D. It converts DC to AC
Correct Answer: C

## Slide 13: Mounting Structure Activity
Activity: “Build the Base”
Materials needed for students:
Wooden sticks / cardboard strips
Nuts-bolts (or paper fasteners)
Uneven surface (book/tilt board)
Activity Steps:
Ask groups to build a small structure
Give them 2 conditions:
  One group builds properly
  One group builds quickly (no alignment focus)
Apply slight pressure or tilt
Discussion:
Which structure was stable?
What went wrong?
Learning:
Alignment matters
Tightening matters
Foundation analogy becomes real

## Slide 14: Panel Placement: Direction & Tilt Optimization
Set correct direction and tilt using compass and inclinometer
Lift and position panels securely on the structure
Video to be embedded PM Surya Ghar Full Video
10:00 seconds to 12:30
Notes: VO: Now watch how the panel direction and tilt are set using simple tools. Also observe how the panels are lifted and positioned properly on the structure.

## Slide 15: Check your Understanding
A technician installs panels facing the wrong direction but with correct tilt. What is the most likely result?
Maximum energy generation
Reduced system efficiency
Better inverter output
No impact on performance
Correct Answer: B

## Slide 16: Check your Understanding
Which tool is commonly used to check proper panel tilt during installation?
A. Clamp meter
B. Inclinometer
C. Tester
D. Wire stripper
Correct Answer: B

## Slide 17: Electrical Installation & System Integration
Perform DC and AC wiring between system components
Install inverter and complete system connections
Video to be embedded PM Surya Ghar Full Video
12:30 seconds to 14:55
Notes: VO: Now observe how electrical connections are made between components. Also watch how the inverter is installed and integrated into the system.

## Slide 18: Check your Understanding
During installation, DC and AC wiring are mixed incorrectly. What is the greatest risk?
A. Reduced sunlight
B. System imbalance or equipment damage
C. Extra battery charging
D. Improved output voltage
Correct Answer: B

## Slide 19: Check your Understanding
A solar system worked properly for two days and then suddenly stopped. Panels are clean and inverter is functioning correctly. What is the most likely issue?
A. Incorrect panel tilt
B. Loose cable connection
C. Excess sunlight
D. Overcharged battery
Correct Answer: B

## Slide 20: Activity: “Failure Investigation”
Scenario: System worked for 2 days, then stopped.
Data given:
Loose cable
Proper inverter
Clean panels
Task:
Identify most likely cause + explain
Learning:
Diagnostic thinking
Real technician skill
Mandavi – How do we plan to do this activity. Also, the answer is already given in the previous CYU.

## Slide 21: Best Practices of Wiring and Distribution board
Connect system to distribution board
Ensure safe and organized wiring
Video to be embedded https://youtu.be/jQ5WB7-ftIs to be merged at 0:42 to 6:20 with https://youtu.be/1hcKMxpyzUw at 1: 02 to 10:15
Notes: Now we connect the system to the distribution board, which sends electricity to different appliances. Observe how the system is connected to the distribution board.
Notice how wiring is arranged neatly and safely.
You can think of it like a main switchboard in a house, where power is safely distributed to fans, lights, and other devices.

## Slide 22: System Inspection & Approval
Inspect installation for safety and compliance
Verify system before approval and operation
Video to be embedded PM Surya Ghar Full Video
14:55 seconds to 22:18
Notes: VO: Now watch how the system is inspected after installation. Observe the checks done to ensure safety and compliance before approval.

## Slide 23: Check your Understanding
Before approving a newly installed solar system, officials mainly inspect for:
A. Decorative appearance
B. Safety and compliance
C. Mobile network signal
D. Weather forecast
Correct Answer: B

## Slide 24: Activity: Connection Check Challenge
Objective: Students identify and fix connection issues
Setup: Use:
  2 wires (or ropes)
  2 labels: “Battery +” and “Battery –”
  1 “Inverter” label
Create 2 setups in front of class:
  One correct
  One with loose / wrong connection
Step 1: Divide class into groups
Each group sends 1 “technician”
Step 2: Task
Technician must: Inspect setup and decide:
Safe / Unsafe
Fix it physically
Step 3: Time pressure
Give 30-45 seconds per student
Step 4: Class votes
Was it correct?
What mistake was there?
Ask:
What was wrong?
What could happen if not fixed?
Learning Outcome
Recognize loose/wrong connections
Take action, not just explain
Understand real-site urgency
Builds confidence

## Slide 25: Earthing & Safety Testing
Test earthing for proper grounding and safety
Ensure system protection against faults and lightning
Video to be embedded PM Surya Ghar Full Video
22:18 seconds to 23:12
Notes: VO: Now observe how earthing is tested for safety. Notice how proper grounding is ensured to protect the system.

## Slide 26: Check your Understanding
What is the primary purpose of earthing in a solar PV system?
A. Increase panel voltage
B. Store backup electricity
C. Provide safe path for fault current
D. Improve battery appearance
Correct Answer: C

## Slide 27: Activity: System Breakdown Simulation
Setup: Give system diagram
Task:
Instructor removes one connection
Students: Predict:
What stops working?
Why?
Learning:
System dependency
Critical thinking

## Slide 28: System Testing - bengali
– to convert to english
Notes: VO: Just like checking a vehicle before driving, testing helps us make sure everything is working correctly and safely. Watch how tests are performed to check if current can flow properly and if there are any faults in the system. Observe how the system is tested before start-up. Notice how checks are done to ensure safe operation.

## Slide 29: Check your Understanding
A technician skips system testing because all connections “look fine.” What is the biggest risk?
A. Faster commissioning
B. Hidden faults may go undetected
C. Improved grid synchronization
D. Better inverter cooling
Correct Answer: B

## Slide 30: Activity: Test or Trouble?
Setup
Write 3 situations on board/cards:
“All connections look fine”
“System just installed”
“Customer wants quick start
Steps
Divide class into groups
Each group must decide: “Start system OR Test first?”
They must:
Stand on one side of room (Start / Test)
Explain why
Twist
Instructor says: “System fails after start — now what?”
Learning
Testing is not optional
Builds decision confidence

## Slide 31: SYSTEM START-UP – Hindi
– to convert to english
Notes: VO: Now observe the correct sequence of starting the system.

## Slide 32: Check your Understanding
Why is the correct start-up sequence important during commissioning?
A. Improves panel cleaning
B. Prevents electrical faults and operational issues
C. Increases structure strength
D. Reduces sunlight dependency
Correct Answer: B

## Slide 33: Activity: Live Sequence Build
Setup: Write steps on paper cards:
Check connections
Switch ON inverter
Start system
Observe output
Steps:
Give cards to different students
Ask them to: Arrange themselves in correct order
Class can:
Agree / disagree
Rearrange physically
Learning
Sequence memory + logic
Movement = engagement

## Slide 34: Net Metering & System Commissioning
Check net meter and grid connection setup
Energize system for electricity generation
Video to be embedded PM Surya Ghar Full Video
23:12 seconds to 27:55
Notes: VO: Now watch how the net meter is checked and connected to the grid. Observe how the system is energized to begin power generation.

## Slide 35: Check your Understanding
What is the role of net metering in an on-grid solar system?
A. Measures rainfall
B. Tracks battery water level
C. Monitors electricity exchanged with the grid
D. Controls panel tilt
Correct Answer: C

## Slide 36: System Handover & Documentation
Complete handover between consumer and DISCOM
Finalize documentation and approvals
Video to be embedded PM Surya Ghar Full Video
27:55 seconds to end
Notes: VO: Finally, observe how the system is handed over after completion. Notice how documentation and approvals are completed at this stage.

## Slide 37: Activity: Risk Ranking
Show 4 issues:
Loose wire
Overloaded DB
Proper earthing
Neat wiring
Task:
Rank from MOST dangerous → least
Learning:
Prioritization
Safety judgement

## Slide 38: Basic Safety Practices in Solar PV work
Start at 1:20 seconds
– to improve to english
Notes: VO: Safety comes first during any installation work. Pay attention to the correct use of PPE and safe working practices on-site.

## Slide 39: Administering First Aid and Fire Safety Protocol
Download and minise the size.
Notes: VO: In case of emergencies, basic first aid and fire safety knowledge is essential. Understand how to respond quickly and handle such situations safely.

## Slide 40: Activity: Safety Inspector
Setup: Create a “fake work area”:
One student without PPE
One loose wire
One unsafe posture
Steps
One student becomes: “Safety Inspector”
They must:
Walk around
Stop work
Identify issues
Others: Defend their actions
Learning
Real-world safety enforcement
Builds confidence to intervene
Notes: Let’s apply what we’ve learned. Identify safety issues in the setup and take action like a real site inspector.

## Slide 41: Preventive Maintenance and Reporting
Observe cleaning and inspection steps
Notice regular maintenance practices
Video to be embedded
https://youtu.be/bw8HreOKFmk (crop 00:20 to 02:09 seconds and merge with the video below in the beginning https://youtu.be/pQAZQOgx9SA 00:42 seconds 07:10
Notes: After installation, the system needs regular care. Just like a bike needs cleaning and servicing, solar panels also need maintenance to work efficiently. Observe how cleaning and inspection help maintain system performance.

## Slide 42: Check your Understanding
A solar system output drops significantly after three months. Panels are dusty and bird droppings are visible. What is the most likely reason?
A. Wrong inverter size
B. Poor preventive maintenance
C. Excess grid voltage
D. Incorrect earthing type
Correct Answer: B

## Slide 43: Activity: Performance Drop Case
Scenario: Output reduced after 3 months
Groups list:
Possible causes
Most likely cause
Learning: Develop Root cause thinking

## Slide 44: Remote monitoring system
End at 6:45 seconds
- Download hindi version
– to convert to english
Notes: Remote monitoring helps track how the system is performing. It’s like checking your mobile battery or data usage. You can see if everything is working properly or if there is a problem.
Just like a bike needs cleaning and servicing, solar panels also need maintenance to work efficiently.

## Slide 45
Course Summary
You understood the complete solar PV installation process
You saw how components are connected and the system works
You learned how installation, wiring, and testing are done
You understood the importance of safety and maintenance
In this course:
Notes: VO: In this course, you have understood the complete process of installing a solar PV system.
You saw how different components are connected, how the system is tested, and how it is safely operated and maintained. This knowledge will help you work more confidently on real installation sites

## Slide 46: Assessment

## Slide 47: Assessment
During rooftop inspection, a technician notices cracks in the mounting foundation. What should be done first?
A. Start panel installation
B. Ignore minor cracks
C. Repair and secure the structure before installation
D. Increase inverter capacity
Correct Answer: C
Notes: Correct Answer: C. Solar Energy

## Slide 48: Assessment
2. Even a loose cable connection can stop an entire solar system from functioning properly.
True
False
Notes: Correct Answer: C. Solar Energy

## Slide 49: Assessment
Column A Column B
1. Earthing A. Safe distribution of power
2. Distribution Board B. Detects insulation leakage
3. Inverter C. Safe path for fault current
4. Insulation Test D. Converts DC to AC
Correct Match:
1 → C
2 → A
3 → D
4 → B
Notes: Correct Answer: C. Solar Energy

## Slide 50: Assessment
4. A system passes visual inspection but fails during testing. What does this indicate?
A. Testing is unnecessary
B. Hidden electrical issues may still exist
C. Panels are oversized
D. Earthing increases voltage
Correct Answer: B
Notes: Correct Answer: C. Solar Energy

## Slide 51: Assessment
5. Which of the following are important during panel placement?
A. Correct tilt angle
B. Proper direction
C. Loose mounting clamps
D. Secure handling during lifting
Correct Answers: A, B, D
Notes: Correct Answer: C. Solar Energy

## Slide 52: Assessment
6. A __________ test checks whether electrical current can safely flow through a circuit.
Answer: Continuity
Notes: Correct Answer: C. Solar Energy

## Slide 53: Assessment
7. Net metering allows excess electricity generated by a solar system to be supplied to the grid.
Answer: True
Notes: Correct Answer: C. Solar Energy

## Slide 54: Assessment
9. A technician notices frequent inverter trips after installation. Wiring appears disorganized and multiple cables are tightly bent. What is the most likely issue?
A. Excess sunlight
B. Improper cable routing and connections
C. High panel efficiency
D. Proper earthing
Correct Answer: B
Notes: Correct Answer: C. Solar Energy

## Slide 55: Assessment
10. Which activities are part of preventive maintenance?
A. Cleaning panels
B. Inspecting connections
C. Ignoring minor faults
D. Monitoring system performance
Correct Answers: A, B, D
Notes: Correct Answer: C. Solar Energy